Saving Power with Wi-Fi:
How to prolong your battery life
and still stay connected
     Vitaly Wool
Senior Consultant, SonyEricsson Mobile Communications

---
WiFi and power saving
- What WiFi is
- WiFi in embedded devices
- WiFi power saving overview
- WiFi software architecture
- Hands-on Android WiFi powersave

---
WiFi: Wireless LAN
- What it does
  - links two or more devices using some wireless distribution method
  - provides a connection to Internet
  - gives users the mobility to move around within a local coverage area and still be connected to the network
- Standards
  - 802.11 – a huge family of standards

---
WiFi: Wireless LAN
- Roles
  - Ad-hoc
    - Used in gaming devices, now obsolete
  - Station
    - “normal” operating mode
  - Access Point (AP)
    - Used to connect stations to wired networks
    - Less of an interest for embedded devices
  - Wi-Fi Direct (P2P)
    - Peer-to-peer

---
WiFi: Wireless LAN
- Frequency ranges
  - 2.4 GHz (802.11bgn), 5 GHz (802.11an)
  - Channels
- Speed
  - Varies from 1 to 600 Mbit/s
- Operation range
  - ≈30 m indoors, ≈100 m outdoors
- Power consumption
  - High, as the speed is high and the range is long

---
WiFi: Wireless LAN
- Why so popular
  - 802.11 is basically “Ethernet over the air”
  - Common hardware
  - Standard TCP/IP stack
  - All LAN services work
- Wi-Fi for embedded
  - Provides internet connectivity without cables
  - Big power consumer
    - Battery life is therefore a big concern

---
WiFi: Wireless LAN
- Wi-Fi station operation modes
  - Tx/Rx
    - Both transmit and receive frames
  - Rx
    - Only receive frames, transmitter may be off
  - Listen
    - Receiver operating on low frequency
  - PS
    - Most of the time off, only wakes up to check for data

---
WiFi and power saving
- What WiFi is
- WiFi in embedded devices
- WiFi power saving overview
- WiFi software architecture
- Hands-on Android WiFi powersave

---
WiFi in embedded devices
- Mainly
  - Tablet devices
  - Mobile phones / smartphones
- But not only
  - Digital Home
  - TV sets and STBs
  - May even be deployed in a fridge :-)

---
WiFi in embedded devices
- Internet connection
  - Wi-Fi is either the only way to or is a preferable alternative to 3G
- User's view
  - We want to stay connected when we don't use the phone
    - Receive emails, Skype calls etc.
  - We don't want to switch to 3G
    - Additional costs involved
  - Bah, we want the battery life to still be long

---
WiFi and power saving
- What WiFi is
- WiFi in embedded devices
- WiFi power saving overview
- WiFi software architecture
- Hands-on Android WiFi powersave

---
WiFi power figures
Mode	Approx. current, mA
Tx/Rx	80
Rx	50
“Listen”	20
Sleep	0.1
- WiFi is very power consuming
  - Up to 80% overall
    for embedded device
- Power saving is crucial for longer battery life
  - 802.11 power save
NB! Real operation over time is always a combination of these modes

---
WiFi Power save objectives
- Can't be saving when transmitting data
- Waiting to receive data most of the time
  - Power saving in this state is crucial
- The main consumer is WiFi radio
  - Switching it off is the best power saving option
- But how will it receive packets then?!

---
802.11 Power Save
- Stations connected to an AP
  - Must notify it before switching the radio off
  - Must wake up at the same time to check for data
    - Receive DTIM from the AP
- If there's data for station in PS mode
  - Either poll the packets one by one
  - ...or move back to radio on and notify the AP
- Synchronization is the key
  - AP and station should be in very good sync for the latter to receive beacons

---
WiFi keep-alive
- Station should send the AP Null packets once in a while
  - AP knows we're alive
  - May help synchronizing
  - Worst case we'll get the disassociation
- On disassociation
  - Re-establish the connection to the AP
  - May not be possible without waking up the host

---
WiFi and power saving
- What WiFi is
- WiFi in embedded devices
- WiFi power saving overview
- WiFi software architecture
- Hands-on Android WiFi powersave

---
WiFi software architecture
- “Soft MAC”
  - MLME implemented in the driver
- “Thick MAC”
  - MLME implemented in the firmware
- Hybrid models
  - Basically Soft MAC with some functionality moved to the firmware
- How do those models differ when it comes to power saving?

---
WiFi chip and host
- Driver runs on host CPU and firmware runs on WiFi chip processor
  - WiFi chip has to wake up host CPU when the firmware can't handle things autonomously
    - e. g. to poll for a data packet
    - Or to handle disassociation
  - Wake-ups may be very frequent
    - NetBIOS
    - SharePort
    - Other perversions

---
Linux kernel WiFi support
- cfg80211: Configuration API
  - Uses nl80211
  - Suitable both for SoftMAC and
    ThickMAC
- Mac80211
  - Implements cfg80211 interface
  - Allows for the driver to be thin
    - Only provides hardware backend

---
Android WiFi architecture
- Looks neat but...
  - wpa_supplicant uses obsolete interface to the kernel (wext)
  - Not much control of PM from the framework
  - No Runtime PM support in the userspace
- Driver has to do a tough job
FRAMEWORK
WifiManager
WifiMonitor
WifiService
JNI
HAL
wpa_supplicant
KERNEL

---
Android WiFi powersaving
- ”WiFi sleep policy”
  - Never
  - When screen goes blank
- Why would we need that?
  - There was no Runtime PM
    in Android historically
  - The kernel driver used was obsolete
  - So it was a mitigation for host wakeups from WiFi
- That's all folks! ©

---
Android WiFi powersaving
- Setting to “when screen
  turns off” is evil
  - Saving the power at a cost
    of connectivity loss
- Setting to “Never” may not
  solve all the problems
  - Keeping the connection is
    much more complicated
- Android framework is not that good at controlling the Wi-Fi power
  - We'll try to get more of it in the driver
:-(

---
WiFi and power saving
- What WiFi is
- WiFi in embedded devices
- WiFi power saving overview
- WiFi software architecture in Android
- Hands-on Android WiFi powersave
  - Keeping the connection
  - Minimizing power consumption

---
Keeping the connection
- The AP should know we're still here
  - Send Null frames once in a while to keep the connection alive
- Reconnect on disconnection
  - Detect and handle
  - More complicated for SoftMAC drivers
    - Happens in WifiStateTracker
    - May be interrupted by PowerManager

---
Conserving power
- Limit the amount of host wake-ups from Wi-Fi
  - Filter ARP in the firmware
  - Filter out uPnP
  - Filter out things like SharePort
- Do not switch on the radio on each beacon
  - Do it on each N-th DTIM
- Do not wake up the host unless really necessary
  - e. g. if there is data pending

---
Result varies on the AP
Average consumption, mA	AP 1	AP 2	AP 3
WLAN chip	1.9	2.8	11.6
Phone, WLAN chip off	2.3	2.3	2.3
Phone, WLAN chip on	5.4	9.7	34.3
WLAN add-up	3.1	7.4	32.0
- WiFi input to power consumption can be really huge
- Very dependent on the AP used

---
Why so sad?
- Bogus wakeups
  - Cranky traffic from APs
- Disassociations
  - Ignoring DTIMs increase this unfortunate chance
    - Especially in “noisy” environments
  - Buggy AP software cause frequent disassociations
- Android architecture
  - Runtime PM unaware
  - Disassociation is handled in WifiStateTracker
    - Too far above, wakes up everything

---
WiFi power saving:
moving forward
- Improvements
  - Better power saving in the chip
  - Delegate more to the firmware
    - Yes, even for Soft MAC
  - Runtime PM
    - Better integration with Android
  - More control from the framework
    - Set power states, Tx Power etc.
    - Use newer wpa_supplicant and nl80211 interface

---
Q&A
?

---
Thanks for your attention!