Comprison of Schedulers and Survey with Real Time Threads
Kenichiro Nakajima
k-nakajima( at mark )tjsys.co.jp
Toshiba Information Systems(JAPAN) Corp.
2006/05/26
(translated by ikoma)

---
Agenda
Background
Objective of Experiments
Environment of Experiments
Surveyed Schedulers
Benchmarks
Discussions
Summary

---
Background
One scheduler for embedded and enterprise? ->Application properties and number of running processes must be different. Maybe, there is no single universal scheduler!?
How about a scheduler for embedded?
Comments welcome!

---
Objectives of Experiments
Study the feasibility of the light-weight, fast scheduler for digital appliances, giving up scalability to some extent
First of all, compare the performance of schedulers
  - To see the difference between handling of non-realtime threads and realtime threads

---
Environment of Experiments
RBTX4400
  - TX4937 300MHz
  - 128MB SDRAM
  - Kernel 2.6.17-rc1 (linux-mips tree)
  - Glibc-2.4 (mips ports)
  - Root FS is on the HDD connected to PCI card
  - Plugsched-6.3.2

---
What is Plugsched?
A patch to make schedulers switchable at boot time by implementing schedulers as drivers
cpusched={ingosched, ingo_ll ,nicksched, staircase}
This enables to tune parameters used for scheduling from sysfs
echo 500 > /sys/cpusched/<sched_name>/<param>
Further, dynsched is a patch to dynamically switch schedulers at runtime

---
Features of Schedulers
Schedulers included in Plugsched-6.3.2
  - ingosched
  - ingo_ll
  - nicksched
  - staircase

---
ingosched
Standard O(1) scheduler
Sets bonus or penalty on priority based on sleep time
Time slices are calculated based on nice values. sprio is the mapped value of nice onto 100..139
alignl minslice = max lbrace 5 * HZ/1000, 1 rbrace newline alignl timeslice = left lbrace stack{ max lbrace 5*HZ/1000*(140-sprio), minslice rbrace ~(nice >= 0) # max lbrace 20*HZ/1000*(140-sprio), minslice rbrace ~(nice < 0)} right rbrace

---
ingo_ll
ingosched with less latency
Under heavy load, ???
No more maintained (I believe)

---
nicksched
Nick Piggin tunes the interactiveness of ingosched
No more maintained either (I believe. Disappeared from Kernel 2.6.4(?))
Priorities are determined based on sleep history
Timeslice is allotted based on the highest priority among the thread's dynamic priority and those included in expired queue
dprio is dynamic priority; minprio is the lowest priority among the running thread and those in expired queue
(60 / (dprio - minprio + 2 ) ) ^{2} * (40 /( 170 - minipri))^{2}*(HZ/1000)/4

---
staircase
Intereactiveness oriented scheduler by Con Kolivas
Under development on ck tree
Set bonus on priority with sleep time
Set penalty on priority with execution time
Get timeslice based on static priority
minslice = left lbrace stack{alignl (6*HZ/1001+1)~~~~~~~~~(nice >= 0) # (6*HZ/1001+1)-(nice)~(nice < 0)} right rbrace newline alignl timeslice = minslice * (1+(19-nice))

---
Benchmarks
Interbench
Hackbench
Original benchmark

---
Interbench
Benchmark to measure interactiveness by Con Kolivas
Measures latancy on scheduling with load emulating X and games

---
Interbench Results (non-RT)
Excerpt from results
load : X window, task : Video

---
Interbench Results (RT)

---
Interbench: Discussions
Staircase performance is remarkable
Here “latency” is defined as time to request cpu till actually getting it
No significant difference for RT
Observing other results, e.g. DeadLines Met keeps high even when I/Os occur, something might be wrong?

---
Hackbench
Tried Hackbench with each scheduler
Hackbench seems to be a benchmark to measure scalability
A number of processes communicate with pipe
Quite heavy as it uses fork()
Number of processes is around 1000

---
Hackbench: Results
Run “./hackbench 30”
Elapsed time (sec)
Ingosched
38.620
Ingo_ll
78.689
Nicksched
45.717
Staircase
43.845

---
Hackbench: Discussions
Ingosched seems to be superior in terms of speed to complete the same amount of tasks
Ingo_ll is a little bit inferior...
The other two are not so bad

---
Original Benchmark
Measures time difference to wake up RT/non-RT thread from RT thread
Uses Hackbench (originating from Interbench) with group 10 as load

---
Configuration of Benchmark
Time Measuring
Thread
Wake up with pthread_cond_broadcast()
RT(Non-RT) Thread
pthread_cond_wait()
till woken up
hackbench 10

---
Results
In case of RT
In case of Non-RT

---
In Case of RT Threads

---
In Case of NonRT Threads

---
Results (RT)
  (usec)
Average
Min
Max
Std Dev
Ingosched
575.03
37
448262
14171
Ingo_ll
386.66
33
82750
4000
Nicksched
119.31
34
1013
120
staircase
167.15
36
66277
2095

---
Results (non-RT)
(usec)
Average
Min
Max
Std Dev
Ingosched
1840.22
38
129328
11304
Ingo_ll
214211.99
152
1554755
192334
Nicksched
117.19
34
1183
115
staircase
162.75
38
1849
177

---
Results: Calibration
Omit data samples beyond 6 sigma, as 1-4 out of 1000 samples are two orders of magnitude larger

---
Results (RT)
(usec)
Average
Min
Max
Std Dev
Ingosched
126.38
37
410
125
Ingo_ll
169.79
33
468
142
Nicksched
116.09
34
473
110
staircase
101.03
36
1092
117

---
Results (non-RT)
(usec)
Average
Min
Max
Std Dev
Ingosched
776.66
38
45828
3742
Ingo_ll
212868.76
152
968781
187688
Nicksched
116.12
34
406
110
staircase
155.49
38
1221
145

---
Original Benchmark: Discussions
Difference of handling of RT and Non-RT tasks
Behavior when fork()ing
Evaluation of processes yield()ed
The difference of obtained timeslices

---
Difference of Handling of RT and Non-RT Threads
Nicksched gives worse result for RT
Might be a bug ...
Frequent sleeping process seems to be treated preferably almost like RT
Depending on situations, rather long timeslices can be obtained
nicksched
Average
Min
Max
Std Dev
RT
119.31
34
1013
120
Non-RT
116.12
34
406
110

---
Behavior when fork()ing
For threads, internally do_fork() is called
With Ingosched, when fork()ing, the parent and child share the time slice
  - For each fork(), the time slice of the parent becomes 1/2 -> Recovered when schedule()ed
    (Prohibiting large number of fork()s in a moment)
  - For the child, penalty is given for sleep evaluation

---
Behavior when fork()ing 2
For nicksched, fork()ing deteriorates the parent's sleep evaluation-> less selection of the parent defers more fork()?
Staircase gives no bonus for the child, but does nothing to the parent -> as dynamic priority monotonically decreases the child can only get minimal timeslices. When fork()ed, the parent can not get bonus until next activate() called

---
Behavior when sys_yield()
Ingosched, Nicksched do nothing special
Staircase sets the dynamic priority highest unless RT
→ A task who yield() is a good task

---
Time Slice
According to NICE Values

---
Tme Slice According to NICE Values (2)

---
Time Slice According to NICE Values (3)
Ingosched, Ingo_ll are as expected because they use a linear function
Staircase is so-so because of square of NICE value at most
Nicksched works based on dynamic priorities, not directly on NICE values. When the highest priority raises by one, timeslices for other tasks become around half. Rather severe for the other tasks than of the highest priority
->While the priorities of load tasks kept lowering, the measured task kept getting more, so the load tasks might hardly be able to run?

---
Summary
Ingosched shows good performance, as well as scalability. But there is considerable latency to wake up non-RT threads
-> Because the priorities of the forked child processes of the load threads are not lowered so much?
For a non-sleeping process, dynamic priority gets lower, but some timeslices can be obtained if nice value is good. Isn't this a problem?
(Although there are exceptional cases,) response less than 1ms can be expected if RT thread used

---
Further Projects(or Daydream?)
To build a new scheduler:
  - Up/down of priority
    - Is dynamic priority really necessary?
      -> Try scheduler with fixed priority?
      -> Try measure time of scheduling related functions, using KFT etc.
      -> Introduce SCHED_INTERACTIVE, for example.
  - Allotment of timeslice
    - Check validity of basing on NICE values
    - Complexity of dynamically setting
  - Control of fork()
    - To avoid fork bomb
  - Evaluation of yield()
Want a method to see dynamic priority any time

---
Image
DPRIO
500ms
1500ms
100
PID
324
468
531
140
533
Visualization of dynamic prority

---
Misc
Other topics

---
At First ...
Could not use sleep-line APIs, as I wanted to wake up processes periodically
-> Sleep allows the process sleep at least for the specified time
  - E.g.
    Say usleep(330000), then, wakes up next time after
    33msec + 1/HZ sec + execution turn comes

---
pthread…
On MIPS, even if pthread_cond_signal() is called, sleeping thread keeps sleeping (bug of glibc-ports)

---
I/O scheduler
Experimented, but got no interesting result. Not reported here.

---
When Priority Changes
Ingosched
  - When sleep (+, -)
Ingo_ll
Nicksched
  - When sleep (+, -)
Staircase
  - When execute (+)
  - When sleep (-)

---
Reference
PlugSched
https://sourceforge.net/projects/cpuse/
Hackbench
http://developer.osdl.org/craiger/hackbench/
Interbench
http://members.optusnet.com.au/ckolivas/interbench/